## Slide 1
Leader Election in Cognitive Radio Networks
Under the guidance of :
Dr. A. K. Singh
Professor
National Institute of Technology, Kurukshetra
Group Number : 1
Harpreet Kaur (110492)
Bhavika (110223)
Shivani (110137)

## Slide 2: Problem Statement
To develop a Leader Election algorithm in Cognitive Radio Networks.
Action Plan adopted:
Studied the transition from static distributed environment to mobile environment and finally to cognitive radio environment.
Studied the existing leader election algorithms in different environments.
Developed an algorithm for leader election in CRN.

## Slide 3: Literature Review in Distributed Networks
Leader Election
Static
Dynamic
Mobile Ad-hoc
Cognitive Radio
Chang and Roberts
Bully
HS
MELFA
ELFA
Algo by N. Mittal, T. Bansal, S.Venkatesan

## Slide 4: Cognitive Radio Network
Allows the unlicensed users to dynamically and opportunistically access the “under-utilized" licensed bands.
Challenges in CRN include dynamic spectrum sensing and heterogeneity of channels. A channel, licensed to a primary node, may not be available for use to a secondary node when it needs to use it. So, it has to dynamically sense the spectrum to find a suitable channel available.
Cognitive Radio:
A cognitive radio is an intelligent radio that can be programmed and configured dynamically.
It can change its transmitter parameters based on interaction with the environment in which it operates.

## Slide 5: Algorithm Concept
The algorithm proceeds in levels of neighbour chaining which represent the levels in a virtual tree.
The virtual tree so formed has the initiator as its root with its neighbours at level 1, neighbours of its neighbours at level 2 and so on.
The initiator starts the election process by sending Election message to its neighbours which continue the process of sending the Election message through forward sweep mechanism.
Continuing in this manner, we eventually arrive at the leaf nodes which start the termination phase by working in backward sweep manner through an End message.
The algorithm terminates when the initiator has received an End message from all its neighbours.
Finally, the initiator with the highest weight and the lowest ID gets elected as the new leader.

## Slide 6
13
11
4
1
16
15
5
9
12
12
Channel busy!!
Waiting for heartbeat for time twait
Here leader starts sensing another option for transmission. It will try upto time tsense
Case 1 : Channel Busy
Triggering Events
Primary node
Secondary node
Leader
Heartbeat

## Slide 7
13
11
4
8
5
7
6
12
12
Leader crashed
Leader Crashed,no heartbeat being received, everybody waiting for the Time_out period
Case 2(a): Leader Crashed.

## Slide 8
13
11
4
8
5
7
6
12
12
Leader moves out
Case 2(b): Leader moves out of system

## Slide 9
13
11
4
1
16
15
5
9
12
12
22
18
4
My weight difference is 3,I have no problem with current leader
I can start as I have greater weight difference
No Problem
At first the new ones ask for leader and then think.
Case 3: When new nodes come in.

## Slide 10
13
11
4
1
16
15
5
9
12
12
Fine with the leader
A
B
If A and B interchange they become primary as shown in next figure and weight change is there.
Case 4: Transformation from primary to Secondary
13
11
32
1
16
15
18
9
12
12
A
B
I can start election as my weight difference is greater than k

## Slide 11
17
42
5
6
23
3
10
42
11
59
90
15
22
38
23
30
Election Message
End Message
Change Message
OK Message
Next Phase

## Slide 12
17
42
5
6
23
3
10
42
11
59
90
15
22
38
23
30
Election Message
End Message

## Slide 13
14
11
10
15
9
Multiple Initiation
50
40
80
65
35
Election message of node 14
Election message of node 15
Receive EM from two initiators id 14 and id 15, as id 15 node has more weight than id 14 so it replies Ok to id 14
80
50
>
OK message
Next phase
Next phase
{14}
{15}

## Slide 14: Analysis
Best Case: The very first node that initiates the election, becomes the leader.
The message complexity is:
num(EM) + num(OK) + num(Change) + num(Next Phase) + num(End) + num(Coordinator)
= n+0+0+n+n+n => O(n)
Worst Case: At first level of every initiation, a new initiator comes up and the old initiator has to terminate its current election process.
The message complexity is:
num(EM) + num(OK) + num(Change) + num(Next Phase) + num(End) + num(Coordinator)
= (n-1 + n-2 + ... + 1) + (n-1) + (n *( n-1)) + (0) + (n) + (n) => O(n2)

## Slide 15: Analysis contd...
Average Case : The new election process would start somewhere near the middle level out of the total levels with respect to the current initiator.
The total no. of nodes till the middle level are:
20+21+…….+2(log2n)/2 = 2(log2n)/2-1 = n1/2 - 1
And since there are log2n levels, the middle level so chosen could be any of these log2n levels. And since the number of nodes at the middle level i.e. at the depth of (log2n)/2 , there are 2(logn)/2 i.e. n1/2 nodes,
So the complexity becomes
(2(log2n)/2-1) * log2n * n1/2 => O(n(Log2n))

## Slide 16: Contd...
Properties proved:
Safety: After termination of leader election protocol, all N-1 nodes in the system agree on the same chosen coordinator.
Liveness: All nodes start election process in Candidacy state and eventually all nodes progress towards Normal state in which all nodes connected to the system agree to the only coordinator.
Termination: The algorithm eventually terminates through the use of “End” message

## Slide 17: References
Bansal, T., Mittal, N., Venkatesan, S.: Leader Election Algorithms for Multi-Channel Wireless Networks. The University of Texas at Dallas (2008).
Akyildiz, I.F., Lee, W.Y., Vuran, M.C., Mohanty, S.: Next generation/dynamic spectrum access/cognitive radio wireless networks: A survey. Computer Networks 50(13), 2127-2159(2006).
Awadhesh Kumar Singh, Shantanu Sharma: Trivial Solution for a Non-Trivial Problem in MANETs. Department of Computer Engineering, National Institute of Technology, Kurukshetra-136119, India.
Awadhesh Kumar Singh, Shantanu Sharma: On Detecting Termination in Cognitive Radio Networks. 2011 17th IEEE Pacific Rim International Symposium on Dependable Computing.

## Slide 18
THANK YOU...